## Slide 1: WP2 Implementation Strategy/Workplan
Task 2.3 Design and specification of SDN interfaces (M06-M21) NXW, TIM, ICCS/NTUA, NBLF
Device Agent
Device Agent
Device Agent
SDN Controller interfaces and device abstract information model:
North-bound interface based on a technology-indipendent REST API (e.g. intent-like) for a relevant set of transport network services and virtual network slicing service
  Possible re-use and extention of result of ongonoing strandarization activities (e.g. Transport API in ONF)
South-bound interface based on a suitable well-knonw protocol (e.g. NETCONF or OpenFlow with optical extension) for configuration and control of optical devices.
  Specific extension for the single devices
Optical devices (Transceivers, ROADMs) abstracted using YANG models and following the disaggregrated modelling paradigm
South-bound Interface (SBI)
North-bound Interface (NBI)
Users, Applications, …

## Slide 2: WP2 Implementation Strategy/Workplan
Task 2.3 Design and specification of SDN interfaces (M06-M21) NXW, TIM, ICCS/NTUA, NBLF
SDN Controller SBI and device disaggregated model:
Single optical devices (e.g. ROADMs) are represented as a composition of multiple sub-components interacting together
Each sub-component can be represented by a proper YANG model in terms of data and functionalities (e.g. commands)
Model-driven
Controller-Agent Interface
c1
c3
c2
Composition of models as representation of device functionality
Impact on Controller SBI (i.e. Controller-Agent interface)
  Standard configuration/control protocols (e.g. NETCONF) extension driven by models.
Model Driven Interface
SDN Agent(s)
SDN Controller
Models (YANG)

## Slide 3: WP[number] Implementation Strategy/Workplan
QAMeleon Plugin
(SBI protocol specific)
Unified NB APIs (RESTCONF)
North-bound Interface (NBI)
South-bound Interface (SBI)
Towards Device Agents
Core Functions:
Topology
Statistics
Flow Mngmt