## Slide 1: Progress on Task 2.3 – NXW

## Slide 2: Task 2.3 - Objectives
Task 2.3 Design and specification of SDN interfaces (M06-M21) NXW, TIM, ICCS/NTUA, NBLF
Device Agent
Device Agent
Device Agent
SDN Controller interfaces and device abstract information model:
North-bound interface:
  Technology Indipendent
  Virtual Network Slicing support
South-bound interface
  Well-knonw protocol SDN (e.g. NETCONF )
  Configuration and control (and monitoring) of optical devices.
Optical devices (S-BVT, ROADMs) abstraction
  Yang models
South-bound Interface (SBI)
North-bound Interface (NBI)
Users, Applications, …

## Slide 3: Task 2.3 – On the interfaces
Controller NBI:
Based on TransportAPI (TAPI)
  Proposed by Open Networking Foundation (ONF)
  Enables programmatic control of network both in a technology-indipent and in a technology-specific fashion
Controller SBI (Controller-Agents):
Should offer functionalities for Configuration, Control, and Monitoring of the optical devices
Configuration:
  Add/Remove/Update
Control
  Modification (optimization) of optical parameters (e.g. Modulation Format)
Monitoring
  Active: Controller periodically retrieves the status of the devices
  Passive: Controller receives advertisements from the agents
NETCONF provides all required functionalities
SDN Agent(s)
SDN Controller
SDN Controller
Users, Applications, …

## Slide 4: Task 2.3 – On the interfaces (Preliminary Work)
Preliminary work has been focused (and will be focused, in the first stage) on the abstraction (modeling) of the optical devices
Model-driven
Controller-Agent Interface
SDN Agent(s)
SDN Controller
NETCONF (RFC6241, RFC6242, …) offers all functionality required to handle a network device
YANG (RFC6020) is a data modeling language for NETCONF:
Models configuration and state data
Models Remote Procedure Calls (RPCs)
Models Notifcations
RFC6244 ”An Architecture for Network Management Using NETCONF and YANG” defines their interaction
Base NETCONF Configuration/Control/Monitoring mechanisms
are shaped by the models

## Slide 5: Task 2.3 – Towards a Sliceable-BTV model
Tx and Rx modules / reconfigurable optical layer parameter
  Narrow linewidth laser / central wavelength {within C-band FlexGrid 12.5 GHz grid}, number of optical flows, number of optical carriers per flow
  Dual polarization transmitter with driving electronics / modulation format {DP-mQAM, Digital subcarrier multiplexing, probabilistic shaping}, number of digital subcarriers, Baud rate
  Polarization diversity receiver / Dual pol signals will always be considered
Presented at 12 Apr FG3 Conference Call

## Slide 6
Task 2.3 - Sliceable-BVT Model - Draft
module: sliceable-bvt_v2
+--rw sbvt
+--rw sbvt-id uint16
+--rw slice-ability-support boolean
+--rw tranceivers* [tranceiver-id]
+--rw tranceiver-id uint32
+--rw optical-flows* [of-id]
+--rw of-id uint32
+--rw optical-flow-carriers* [ofc-id]
+--rw ofc-id uint32
+--rw frequency-info
| +--rw base-central-frequency frequency-ghz-type
| +--rw base-central-frequency-granularity frequency-ghz-type
| +--rw central-frequency-slot-granularity frequency-ghz-type
| +--rw n int16
| +--rw m int16
+--rw subcarrier-modules* [subcarrier-id]
+--rw subcarrier-id uint32
+--rw direction direction-type
+--rw baud-rate baud-rate-type
+--rw modulation modulation-type
+--rw central-frequency frequency-ghz-type
SBVT is the main container consisting of:
    An ID (unique)
    An Array of Tranceivers
Optical flow:
    ID (unique)
    Array of Optical Carriers
Optical Carrier:
    ID (unique)
    Frequency Info:
      Flex-Grid (ITU-T G.694.1)
      Base-central-frequency: 193100 GHz
      Central-frequency-granularity: 6.25 GHz
      Slot Granularity: 12.5 GHz
      n: to fix the nominal central frequency
      m: to fix the carrier width
    Array of Subcarriers
Subcarrier:
    ID (unique)
    Direction (TX, RX)
    Other: Baud-rate, modulation format and central frequency
Tranceivers:
    ID (unique)
    Array of Optical Flows
Plenary meeting, Berlin 22-23 May 2018

## Slide 7
Task 2.3 – Towards a ROADM model
High speed 1x4 WSS
  Reconfigurable optical parameters: Input port, output port(s), spectrum slot in multiples of 12.5 GHz, center frequency of port
1x24 WSS
  Reconfigurable optical parameters: Input port, output port(s), spectrum slot in multiples of 12.5 GHz, center frequency of port
8x24 Transponder Aggregator (TPA)
    Reconfigurable optical parameters: output port(s) (ADD/DROP), spectrum slot in multiples of 12.5 GHz, center frequency of port
7
Presented at 12 Apr FG3 Conference Call
Plenary meeting, Berlin 22-23 May 2018

## Slide 8
Task 2.3 - ROADM Model (road to): WSS - draft
module: wss
+--rw wss
+--rw wss-id uint32
+--rw wss-direction direction-type
+--rw wss-number-of-ports uint32
+--rw wss-speed boolean
+--rw wss-ports* [port-id]
+--rw port-id uint32
+--rw port-direction direction-type
+--rw port-center-frequency frequency-ghz-type
+--rw port-frequency-slots uint16
N Ports
1xN
WSS
In case of 1x4 WSS, Output direction (4x1), we will have:
5 Ports:
  4 Input Ports: direction towards the wss
  1 Output Port: direction outwards the wss
Plenary meeting, Berlin 22-23 May 2018

## Slide 9
Task 2.3 - ROADM Model (road to): TPA - draft
module: tpa
+--rw tpa
+--rw tpa-id uint32
+--rw tpa-direction tpa-direction-type
+--rw tpa-number-of-inports uint32
+--rw tpa-number-of-outports uint32
+--rw tpa-ports* [port-id]
+--rw port-id uint32
+--rw port-direction tpa-port-direction-type
+--rw port-center-frequency frequency-ghz-type
+--rw port-frequency-slots uint16
In case of 8x24 TPA, Drop, we will have:
32 Ports:
  8 Input Ports: direction towards the tpa
  24 Output Ports: direction outwards the tpa, towards transponders
M Ports
N Ports

## Slide 10
Task 2.3 - ROADM Model (road to): reference models
QAMeleon ROAD proposal
Example of 4-degrees ROADM
Plenary meeting, Berlin 22-23 May 2018

## Slide 11
ROADM Model: a possible solution
(A)
module: roadm
+--rw roadm
+--rw roadm-id? string
+--rw directions* [direction-id]
+--rw direction-id uint32
+--rw direction-switches* [wss-id]
+--rw direction-tpas* [tpa-id]
TPAs are part of each ROADM degree.
A ROADM is modeled as a set of Directions/Degrees
Each Direction/degree includes a list of WSS and a List of TPAs

## Slide 12
Task 2.3 - ROADM Model: Alternative Solution
(B)
module: roadm
+--rw roadm
+--rw roadm-id? string
+--rw directions* [direction-id]
| +--rw direction-id uint32
| +--rw direction-switches* [wss-id]
+--rw tpas* [tpa-id]
TPAs are NOT part of ROADM degree.
A ROADM is modeled as a set of Directions/Degrees and a set of TPAs
Each Direction/degree includes a list of WSS
Plenary meeting, Berlin 22-23 May 2018

## Slide 13
Task 2.3 - ROADM Model: components wiring and lightpaths
Plenary meeting, Berlin 22-23 May 2018
Physical connection between ROADM components:
  Needed to know what resources Optical HW offers in terms of available path for the light
Lightpaths:
  Connections in use
In a network of N devices:
Is it a scalable approach?
Is a single instance of SDN controller enough to handle such complexity?
Discussion is still in progress
Possible solutions:
More models per device with different levels of abstraction
Controller hiearchy
  e.g. one controller for a small set of devices and one which handles the network domain
Potential risk: the proposed centralized architecture may need to evolve in a «hierarchical» architecture.
 More complexity for a scalable deployment (not an issue for demos)

## Slide 14
Task 2.3 – On ROADM modeling: OpenROADM MSA
From OpenROADM web site (http://www.openroadm.org) :
14
Plenary meeting, Berlin 22-23 May 2018
“The Open ROADM Multi-Source Agreement (MSA) defines interoperability specifications for Reconfigurable Optical Add/Drop Multiplexers (ROADM). Included are the ROADM switch as well as transponders and pluggable optics. Specifications consist of both Optical interoperability as well as YANG data models”
OpenROADM defined a set of usefull yang models can be reused in QAMeleon
Telecom Italia is a memeber of the agreement

## Slide 15
Task 2.3 – On D2.2: ToC Proposal – SDN section
As T2.3 will start at [M6], D2.2 (due at M8) will cover only 2 of the 15 months of the task.
Proposed SDN Section ToC (both SBVT and ROADM):
State of the art for SBVT and ROADM modelling and control - NXW, NTUA, TIM
  Existing projects (ORCHESTRA, NEPHELE for agent) - NXW, NTUA, TIM
  Paper references - NXW, NTUA
  Effort on modelling: Standard, Consortium, etc (IETF, OpenROADM, ...) - NXW
SDN-based architecture for controlling SBVT and ROADMs - NXW
  Disaggregated modelling approach
  General components and reference points
    SDN controller + SDN agent
    Abstract messages
  Controller SBI
    Short discussion on protocol alternatives, motivation for NETCONF – NXW
    Interaction with proprietary devices with embedded controllers - TIM
    YANG models draft - NXW
  Interface between SDN-Agent and hw (via FPGA) – NTUA/NXW
  Initial implementation design (i/f, NETCONF modules, etc.) - NXW
15
Plenary meeting, Berlin 22-23 May 2018
Probably this deliverable is too early for implementation and integration issues. This needs further discussions in WP7.

## Slide 16
Task 2.3 – Progress, risks & plans for next 6 months
Plans:
Close interaction with FG3 partners (expecially NTUA and TIM) both offline and telcos to:
  Definition and practical solution for Agent-FPGA communication interface
  Definition of interface between agent and TIM Roadm solution
  Periodically check of progresses on models (SDN functionalities, parameter correctness, etc)
    Proposed models include only the configuration part
      Status and Notification are still missing
Progress:
Expected to have a quite stable model for both S-BVT and ROADM
  Preliminary skeleton of the agent(s)
16
Plenary meeting, Berlin 22-23 May 2018